## Slide 1: MS Template Creator Summary
  Input Raw data
MRM transition names data form | Compulsory column names | Restricted column names
Agilent’s WideTable form | Data File (from Sample) | Quantitation Message (from Sample) Columns from Qualifier Methods ISTD Compound Methods ISTD Compound Results
Agilent’s CompoundTable form | Name (from Compound Method) Data File (from Sample) | Quantitation Message (from Sample) Columns from Qualifier Methods Qualifier Results ISTD Compound Methods ISTD Compound Results
  Example
  Transition Name Annotation (cont)
  Validation
Click on the button below to check if ISTD is valid
  Transfer ISTD for annotation
Click on the button below to transfer the ISTD to the ISTD_Annot sheet
  Table of valid MRM data formats
  Input Tabular data
  Example
Samples as rows. Transitions as columns
Transitions as rows. Samples as columns
Conversion of concentration values from nM to other units are available
  Transition Name Annotation
  Load Transition Names
Click on the button below to load the transition names
  ISTD Annotation
  ISTD concentration calculation
Click on the button “Convert to nM and Verify” to change the given ISTD calculations from ng/mL to nM. Users may key in the concentration in nM directly as well.
  Sample Annotation
  Create a new Sample Annotation
Choose the Sample type
Fill any blank cells under the Sample_Type column with “SPL” by clicking this button.
Click on the button below to create a new sample annotation
Fill in the sample amount, unit and ISTD mixture volume
Fill in the concentration unit by clicking this button
Concentration unit is determined by what is provided in the following columns
Updated: 2021-09
For Sample_Type with consistent values, click on this button
Fill in the values and click on the respective “Autofill” buttons

## Slide 2: MS Template Creator Summary
Updated: 2021-09
  Sample Annotation (cont)
  Copy RQC Samples to Dilution Annotation
Create a new sample annotation with RQC samples.
  Dilution Annotation
  Dilution Information
Click on the button below to copy RQC samples to Dilution Annotation
User will fill in the dilution batch name , the relative sample amount in % and Injection volume in uL
Merging with an existing sample annotation file
Insert MRM data and sample annotation file
Map the detected column and merge the data
Check if merge is successful for every row